Devising an explicit algorithm based on simple rules is difficult! L1 reg: \ell = err(y,\hat{y}) + \lambda \sum^N_{i=1}|w_i| favours few non-0 coefs, L2 favours small coefs

under-fitting → high bias (high training, high test error) → add features, decrease regularization term λ, increase degree of polynomial)
over-fitting → high variance (low training, high test error) → get more data, remove features, increase regularization term λ, decrease degree of polynom)

Challenges in Semantic Segmentation (every pixel in an image belongs to a class)
- noise – high-frequency pixel variability (not relevant/may obscure target)
- partial volume – quantized version of object (pixels may contain mix of two objects and both contribute to pixel value) and object may be elevated (unclear where to begin/end object)
- intensity inhomogeneities – varying contrast and intensity differences across the image plain
- anisotropic resolution – (not isotropic, where voxels are cubes) causes \downarrow clarity in coarse dims

- imaging artifacts – implants may interfere with imaging modality
- limited contrasts – different tissues may have similar physical properties and leak boundaries
- morphological variability – variability in physiological conditions or imaging modalities
Output size = , # of param C \times K \times K

Expert Gold Standard: \times training, tedious, intra (same dude) + inter (diff dude) observability variability, \surd multiple segmentations, agreement can be quantified

- specificity = \frac{TN}{N} = \frac{TN}{TN + FP}

- Fβ = (1+\beta^2)\frac{Precision \cdot Recall}{(\beta^2 \cdot Precision) + Recall}

- Jaccard Index/ IoU = \frac{|S_g\cap S_p|}{|S_g \cup S_p|} = \frac{DSC}{2-DSC}

- Dice Sim. Coeff. = 2\frac{|S_g\cap S_p|}{|S_g|+|S_p|} = F_1

- Volume Sim = 1 - \frac{||S_g| - |S_p||}{|S_g| + |S_p|} = 1 - \frac{|FN - FP|}{2TP + FP +F FN}

surface distance measure
Hausdorff Distance =
  \max(h(A,B),h(B,A)), h(A,B) = \underset{a\in A}{\max} \underset{b\in B}{\min} ||a-b||

Average Surface Distance (create map and swap)
  \frac{d(A,B)+d(B,A)}{2}, d(A,B)=\frac 1 N \sum_{a \in A} \min_{b \in B} ||a - b||

Pitfalls in Segmentation Evaluation
- Structure Size – equal differences between small and big structures change spatial overlap lots
- Structure Shape – spatial overlap metrics are unaware of complex shapes
- Spatial alignment – HD & DSC & IoU don’t capture object centre point alignment
- Holes – Boundary-based metrics ignore overlap between structures
- Noise – Affects HD as it is spiked by a far away FP
- Empty Label-Maps – scores of 0 or NaN for each method with combo of empty ref. or predict.
- Resolution – same prediction shapes at different resolutions give different results
- Over vs Under-segmentation – for equal HD, DSC may be better for over than undersegment.

Multi-scale processing: 4 layers of 5^3 kernels followed by 1^3 kernel for classification. Multiple pathways for different sized snippets of the image. Then we concat. Feature maps from both pathways

Vision transformers: split image into patches, encode location, get hidden feature after convolutions, linear layer and pass through attention network similar to nlp. Upsample in U-net fashion with connections.

Segmentation Methods
- Intensity Segmentation: (hist) \times regions must be homogenous, leakages, threshold loc. Hard

- Region Based: (start from seed) \times requires user points, leakages, assumed homogeneity

- Atlas Based: (averaged templates) Registration: mutate multiple atlases into target and fuse labels (majority voting) (this saves pdf indicating contention between sources). \surd robust, accurate, automatic \times comput, expensive, poor for abnormalities, not for tumour segmentation.

- Random Forests: different modalities of 1 image, construct a tree to classify a pixel based on rules. Ensemble it by averaging answer of many trees. \times no hierarchal features \surd || & accurate

- (up)pooling and max (un)pooling with stored spatial location
- Transposed Convolution:
  (M-1)\times S - 2P + D\times(K-1)+P_{output}+1

- Convolution: \left\lfloor \frac{M+2P-D*(K-1)-1}{S} \right\rfloor + 1

- Atrous spatial pyramid pooling: repeated max-pooling and striding reduces spatial resolution of the resulting feature map
- Padding during upsampling may introduce artifacts